## Slide 1: Final Project Embedded System for E-Health
Apicella Salvatore, Bove Simone, Cascone Maria a.y. 2022/23

## Slide 2: INTRODUCTION
As final project of the course we must to crate with STM32 a smart medical device avoid to monitoring and raise an alert about temperature, heart rate and blood oxygen rate.

## Slide 3: NUCLEO F4 AND PERIPHERALS
NUCLEO F401RE
The main board
MAX32664
HR and SPO2 Sensor
KY028
Temperature ADC sensor
SSD1306
Oled screen
DS1307
External CLock
BUZZER
LED

## Slide 4: Circuite in Fritzing

## Slide 5: SW ARCHITECTURE
USE OF SINGLETON
USE TIM CALLBACK
NEVER USE WHILE(1)

## Slide 6
USE OF SINGLETON

## Slide 7: SW INTERFACES
To generate an interrupt every millisecond: pre scale 1, period 7999
UART
ADC
For temperature sensor, Continuos Conversion Mode
I2C
Only one bus is used for pilot 3 devises
TIM 11
  TIM 1 FOR PWM
TIM 10
Used for debug, baud rate 9600 bits/s
2 different channels set by code, used to pilot led and buzzer
To generate an interrupt every second: pre scale 1599, period 9999
04
05
01
02
03
06

## Slide 8: TIM 10
READ DATA
TRIGGER FLAG
RAISE ALERT
MAIN IF STATEMENT
if (htim->Instance == TIM10){}
if (htim->Instance == TIM11){}
SW PROTOCOLS
MANAGE ANIMATION
TIM 11

## Slide 9: POWER DISSIPATION
Device | Power | Energy
NUCLEO | 29.43 mW | 1340 mWh
KY028 | 0.080 mW | 
MAX32664 | 1305 mW | 
SSD1306 | 1.419 mW | 
DS1307 | 4.95 mW | 
LED | 7.5 mW | 0.125 mWh for cycle
BUZZER | 13.61 mW | 0.019 mWh for alarm

## Slide 10: THANKS!
Do you have any questions?